Math 11 At Work Chapter 7 Review

Multiple Choice

Identify the choice that best completes the statement or answers the question.

____	1.	Which of the following cannot form a right-angle triangle? A triangle with side lengths of:

| a. | 11 cm, 60 cm, and 61 cm. | c. | 37 mm, 35 mm, and 12 mm. |
| --- | --- | --- | --- |
| b. | 18 m, 24 m, and 30 m. | d. | 77 m, 34 m, and 111 m. |

____	2.	In a right triangle, angle A is 27°. If that angle is increased, at which angle measure will the value of tan A be double the value of tan 27°?

| a. | 46.6° | c. | 45.5° |
| --- | --- | --- | --- |
| b. | 44° | d. | 48.7° |

____	3.	How long is a ladder that reaches a height of 4.36 m at an angle of elevation of 74°?

| a. | 4.54 m | c. | 3.24 m |
| --- | --- | --- | --- |
| b. | 15.82 m | d. | 1.25 m |

____	4.	A construction company is assembling a slide in a children’s playground. The slide is 7.4 m long. If the slide can have a maximum slope of 27°, how high can the top of the slide be?

| a. | 3.4 m | c. | 3.8 m |
| --- | --- | --- | --- |
| b. | 2.3 m | d. | 6.6 m |

____	5.	What does a clinometer do?

| a. | It measures the height of an object or the length of an object. |
| --- | --- |
| b. | It measures the angle of elevation or depression of the line of sight. |
| c. | It measures the distance between any two objects at sea level. |
| d. | It measures the altitude or depth compared to sea level of a nearby object. |

____	6.	What is the minimum length of a wheelchair ramp, if it must rise a height of 1.3 m at a maximum angle of 9.4° above the horizontal?

| a. | 7.96 m | c. | 1.32 m |
| --- | --- | --- | --- |
| b. | 0.21 m | d. | 7.85 m |

____	7.	The Statue of Liberty is 305 ft tall, from the ground to the top of her torch. If you stood 80 ft away and used a clinometer to view the top of the statue, what would the clinometer read?

| a. | 14.7° | c. | 75.3° |
| --- | --- | --- | --- |
| b. | 74.8° | d. | 15.2° |

Short Answer

8.	The largest drop on a roller coaster has a slope of 64° above the horizontal and covers a distance of 13 m on the ground. How tall is the roller coaster at its peak?

9.	The sun is shining at an angle of elevation of 32°. If a building casts a 65-metre long shadow, how tall is the building?

10.	A long tunnel is being constructed to allow safe travel for transport trucks through a mountain range. If the road through the tunnel can only be 10° steep and has to carry trucks up a height of 1120 ft, how long will the road be?

11.	An new highway off-ramp is being constructed along a stretch of 31.1 m of land and it needs to drop a height of 4.1 m. What will be the angle between the off-ramp and the ground?

12.	Starting at point 1, connect the four dots in order from 1 to 4. What is the length of the shortest path that achieves this?

Long Problem

13.	A garden is cordoned into three sections, as shown in the diagram. What is the perimeter of the garden?

14.	 Solve for x.

15.	A 11-foot ladder is leaning against a vertical wall. For the ladder to be used safely, it cannot be placed at an angle of elevation of less than 63° or greater than 80°. What range of heights can the ladder safely reach?

16.	A surveyor is measuring the heights of various buildings. From the top of one building, the angle of elevation to the top of the neighbouring building is 20° and the angle of depression to the bottom of the building is 74°. If the neighbouring building is 11 m away, how tall is it?

17.	A billboard is mounted high on the side of a building. At a distance of 102 ft from the building  (distance b), the angle of elevation to the bottom of the billboard is 53° (angle ), and the angle of elevation to the top of the billboard is 5° more.

How tall is the billboard (x)?

18.	Stella is calculating the height of a Douglas fir tree that she can see from her campsite. From her tent, she measures the angle of elevation to the top of the tree to be 23°. She then walks 55 m closer to the tree and measures the angle of elevation to be 34°.

a) 	Draw a diagram showing the situation.

b) 	How far from the tree did Stella take her first measurement?

c) 	What is the height of the tree?